## Slide 1
Prakash Rao Dunaka and Bruce McMillin
Department of Computer Science
Missouri University of Science and Technology
Rolla, MO 65401 USA
ff@mst.edu, +1573-341-6435
Cyber-Physical Security of A Chemical Plant

## Slide 2: What is a Chemical Plant?
A chemical plant is typically an industrial process plant that manufactures or processes chemicals on a large scale.
Raw materials
Output
Operations
Control Unit

## Slide 3: Why is Security Important?
Integrity (safety, product quality, financial loss)
Confidentiality (design documents, formulas and manufacturing process)

## Slide 4: How to address security?
By developing effective security models.
By examining stuxnet-like attacks and their impact.
Security models will be addressing the potential and limitations of an attack.

## Slide 5: Non-deducibility
Non-deducibility
  Good?
  - Bad?
Secure Domain
Open Domain
Open Domain
Inside Domain
Non-deducibility is a bidirectional model.

## Slide 6: The Challenge
Prevent the bad guys from seeing confidential/private information.
Make sure the good guys can deduce that an attack is happening from the bad guys
In a CPS
With the same model

## Slide 7: Our Approach : Multiple Security Domain Nondeducibility ( MSDND)
MSDND:
There exists some world with a pair of states where one must be true and the other false (exclusive OR), but an entity i has no valuation function for those states. In security domain SDi, i simply cannot know which state is true and which is false.
Mathematically,
MSDND (ES) = ∃w ∈ W ⊢ [(sx ∧ sy)] ∧ ~( sx ∧ sy) ∧ [w ⊢( ∄Vxi (w)∧ ∄Vyi (w) )]
An equivalent formula is
MSDND (ES) = ∃w ∈ W ⊢ [(sx sy)] ∧ [w ⊢(∄Vxi (w)∧ ∄Vyi (w) )]
If a System is MSDND secure- It is BAD for the system
If a System is Not MSDND secure- It is GOOD for the system
⊕

## Slide 8
It is bad for the system if it is MSDND secure with respect to integrity since by the deﬁnition of MSDND the observer does not have valuation functions for the states of the system i.e. he cannot determine which state is true and which state is false (he cannot determine if there is any change in information).
However it is good for the system with respect to conﬁdentiality because any observer will not be able to know any changes made to the system.

## Slide 9: Case Study: Benzene Plant
Toluene + H2  Benzene + CH4 + Energy

## Slide 10: Information flow paths in the plant
Level, Pressure, Flow, and Temperature Information paths
E
Element
T
Transmit
PLC
CV
Control Valve
Operator
RC
Relay/
Compute
AH
Alarm High
AH
Alarm Low

## Slide 11: Attack Model: Stuxnet-like
Reactor(R-101) and Phase Separator (V-102)
Security Domains of pressure information path

## Slide 12: under attack (no alarms) : Pressure is not normal
Claim: Pressure information is MSDND secure.
Proof:
PLC
BUFFER
STUXNET-like
Transmitter
Sensor
P
I3,0~P
B3I3,0~P
T3,0~P
P
~P
P
I2,3P
B2I2,3P
T2,3P
B3~P

## Slide 13: Continued..
Since B2I2,3p ∧ T2,3p → B2p, the PLC believes the lie told in step 7 in all cases. Therefore, unknown to entities in SD2, V2p (w) and V2∼p (w) cannot be evaluated. Therefore p is MSDND secure from SD2.
BAD for the plant. Threat goes undetected

## Slide 14: Under attack with physical alarms in place
Corollary: If the alarms are working, then pressure information beyond the threshold will make the alarm go off which will make the information not MSDND secure.
Proof:
12. MSDND (ES) = ∃w ∈ W ⊢ [(Sp XOR S~p)] ∧ [w ⊢(∃ V~p5 (w)∧ ∄Vp5 (w) )]
V~p5 (w)exists: this contradicts the second part of the MSDND definition.
PLC
BUFFER
STUXNET-like
Transmitter
Sensor
P
I3,0~P
B3I3,0~P
T3,0~P
P
~P
P
I2,3P
B2I2,3P
T2,3P
B3~P
I1,0~P
B1I1,0~P
T1,0~P
I5,2~P
B5I5,1~P
T5,1~P
Alert Mismatch

## Slide 15: Continued..
Since B5I5,1~p ∧ T5,1~p → B5~p. Therefore, in SD5, V5∼p (w) can be evaluated. The Operator knows that pressure is not in desired range. Therefore p is not MSDND secure from SD5.
GOOD for the plant. Threat can be detected.
Conclusion:
If there is a physical alarm on the information path and an entity ’i’ looks because he or she does not trust the electronic reports, the pressure of the vessel is not MSDND secure with respect to any entity that checks the physical alarm

## Slide 16: Interaction between the Reactor and Phase Separator:
Reaction being exothermic, hydrogen is compressed and recycled back to the reactor via Phase Separator (V-102) to control the temperature.
Invariant is a function, quantity, or property that remains unchanged when a speciﬁed transformation is applied.
Invariant equation:
TR-101 = Ts6 + Treaction – Ts7
TR-101 is out of range  Ts6 or Ts7 is faulty or both are faulty or the sensor at TR-101 is faulty.
TR-101 | Temperature of the Reactor
Ts6 | Temperature reduction due to pumping of H2 (Stream 6)
Treaction | Rise in temperature due to reaction
Ts7 | Temperature of the inputs ( Stream 7)

## Slide 17: MSDND in temperature information path
Case a: Suppose Ts7 is faulty and as result temperature is out of range (alarm beeps)
Proof:
12. MSDND (ES) = ∃w ∈ W ⊢ [(St XOR S~t)] ∧ [w ⊢ (∃ V~t5 (w) ∧ ∄Vt5 (w) )]
V~t5 (w)exists: this contradicts the second part of the MSDND definition
PLC
BUFFER
Transmitter
Sensor
~t
I3,0~t
B3I3,0~t
T3,0~t
~t
~t
~t
I1,0~t
B1I1,0~t
T1,0~t
I5,2~t
B5I5,1~t
T5,1~t

## Slide 18: Continued..
Since B5I5,1~t ∧ T5,1~t → B5~t. Therefore, in SD5, V5∼t (w) can be evaluated. The Operator knows that temperature is not in desired range. Therefore t is not MSDND secure from SD5.
GOOD for the plant. Threat can be detected.

## Slide 19: Continued..
Case b: Suppose Ts7 is faulty and temperature is in desired range (alarm does not beep).
Proof:
12. MSDND (ES) = ∃w ∈ W ⊢ [(St XOR S~t)] ∧ [w ⊢ (∄ V~t5 (w) ∧ ∄Vt5 (w) )]
PLC
BUFFER
Transmitter
Sensor
t
I3,0t
B3I3,0t
T3,0t
I1,0t
B1I1,0t
T1,0t
t
t
I1,0t
B1I1,0t
T1,0t
I5,2t
B5I5,1t
T5,1t
~t Not desired but in range
B1t
B5t

## Slide 20: Continued..
Unknown to entities in SD5 (operator), V5t (w) and V5∼t (w) cannot be evaluated. Therefore, t is MSDND secure from SD5. The temperature is consistent with both working and non-working states of the system.
BAD for the Plant. Since a potential threat cannot be detected.
However when we take the invariant into consideration:
14. I5,6 t Operator observes the invariant
15. B5I5,6 t Operator believes invariant
16. T5,6 t Operator trusts invariant
17. B5I5,6t ∧ T5,6t → B5t Operator believes readings are correct and normal
18. SInv ∧ St = S” Normal working if and only if this is true.
19. w ⊧ V5~t (w) = true
MSDND (ES) = ∃w ∈ W ⊢ [(S” XOR S~t)] ∧ [w ⊢ (∄ V~t5 (w) ∧ ∃ Vt5 (w) )]
Vt5 (w)exists: this contradicts the second part of the MSDND definition
PLC
BUFFER
Transmitter
Sensor
t
I3,0t
B3I3,0t
T3,0t
I1,0t
B1I1,0t
T1,0t
t
t
I1,0t
B1I1,0t
T1,0t
I5,2t
B5I5,1t
T5,1t
~t Not desired but in range
B1t
Mismatch
TR-101 = Ts6 + Treaction –Ts7
I5,6t
B5I5,6t
T5,6t

## Slide 21: A Few Other invariant equations
The overall material balance for the benzene process.
Input = Output
Stream 3 + Stream 1 = Stream 15 + Stream 16.
[Toluene feed + Hydrogen feed] == [ Benzene produced + Fuel gas produced]
Conversion per pass of toluene to benzene in R-101
Toluene introduced= 144 (Stream 6) + 0.04 (Stream 7) = 144.04 kmol/h
Benzene produced= 116 (Stream 9) − 7.6 (Stream 6) − 0.37 (Stream 7) = 108.03 kmol/h
ε= 108.03/144.04 = 0.75
Alternatively, the following can be written:
Moles of benzene produced= Toluene in - Toluene out == 144.04− 36.00 = 108.04 kmol/h
ε= 108.04/144.04 = 0.75

## Slide 22: conclusions:
 | Stuxnet attack on Pressure path |  | 
information path | Case | Result | Inference
Pressure path | under Attack/ No alarms | MSDND secure | BAD for the plant
Pressure path | under attack with physical alarms | Not MSDND secure | Good for the plant
Temperature path | temperature out of range | Not MSDND secure | Good for the plant
Temperature path | temperature with in range | MSDND secure | BAD for the plant
MSDND is useful to model attacks where the goal is to hide critical information from an operator rather than to steal information.
If a System is MSDND secure- It is BAD for the system
If a System is Not MSDND secure- It is GOOD for the system
A system without any MSDND secure information ﬂows between the CPS and cyber monitors has fewer weaknesses which can be exploited.
Temperature path | temperature with in range with Invariant in place. | Not MSDND secure | Good for the plant, threat can be detected

## Slide 23: Future work:
can MSDND be extended and applied to the connected processing units.
effect of a single attack on all other connected processing units.
to detect the easiest information path that an attacker can disrupt to have maximum impact and how to counter such attacks.

## Slide 24
Prakash Rao Dunaka and Bruce McMillin
Department of Computer Science
Missouri University of Science and Technology
Rolla, MO 65401 USA
ff@mst.edu, +1573-341-6435
Cyber-Physical Security of A Chemical Plant